## Slide 1: What is DHT?

## Slide 2: INTRODUCTION
DHT is basically Temperature & Humidity sensor. The DHT sensors are made of two parts, a capacitive humidity sensor and a thermistor. We have a two versions of the DHT sensor and they are;
DHT11
DHT22

## Slide 3: Introduction
  DHT11 Temperature & Humidity Sensor feature a temperature & humidity signal acquisition complex with a calibrated digital signal output. By using the exclusive digital-signal-acquisition technique and temperature & humidity sensing technology, it ensures high reliability and excellent long term stability. This sensor include a resistive type humidity measurement component and a NTC temperature measurement component, connect to a high performance 8-bit microcontroller, offering excellent quality, face response, anti-interface ability and cost effectiveness. It’s of small size, low power consumption and up to 20 m signal transmission makes it a best choise for various applications.

## Slide 4: Features
DHT series digital temperature & humidity sensor.
Full range of calibration, in-line digital output;
Humidity measuring range:20% to 90% RH
Temperature measuring range:0 to 50 0C;
Humidity measurement accuracy: 5.0% RH
Temperature measurement accuracy: 2.0
Low power consumption.
Power:3.5 -5V.
The sampling period of the sensor is 1 second.

## Slide 5: DHT11 SENSOR
DHT11 sensor consists of 4 pins:
VCC
Data
Not Connected(NC)
GND.
The range of voltage for VCC pin is 3.5V to 5.5V. A 5V supply would do fine.
The data from the Data Out pin is a serial digital data.
The data from the sensor consists of integral and decimal parts for both Relative Humidity(RH) and temperature.
The data from the DHT11 sensor consists of 40- bits and the format is as follow:
8-Bit data for integral RH value, 8-Bit data for decimal RH value, 8-Bit data for integral Temperature value, 8-Bit data for decimal Temperature value, 8-Bit data for checksum.

## Slide 6
Example
Consider the data received from the DHT11 sensor is;
00100101 00000000 00011001 00000000 00111110.
In order to check whether the received data is correct or not, we need to perform a small calculation. Add all the integral and decimals values and check whether the sum is equal to the checksum value i.e. the last 8-bit data.
00100101+00000000+00011001+00000000 =00111110
The value is same as checksum and hence the received data is valid. Now to get RH and Temperature values, just convert the binary data to decimal data.
RH= Decimal of 00100101= 37%
Temperature = Decimal of 00011001= 25 0C

## Slide 7: Interfacing With Board And Reading Value

## Slide 8: Circuit Diagram

## Slide 9: Application
DHT11 Relative Humidity and Temperature sensor can be used in many applications like;
HVAC(Heating, Ventilation and Air conditioning) system.
Weather Stations.
Medical Equipment for measuring humidity.
Home Automation systems.
Automotive and other weather control applications.

## Slide 10: Advantages
It does not require any maintenance for longer periods.
Flexibility to use.
Low cost.
Atm. Pressure independent, it work when pressure is being applied.

## Slide 11: Disadvantage
  Some time it quite slow.